# CONSTRUCTION     PRICE     INDEX

( Input Cost  Index for the construction of a single storey house )

2nd Quarter 2010

- Introduction

This issue of the Economic and Social Indicators presents the monthly Construction Price Index (residential) for the second quarter of 2010 with second quarter 2009 as base period. Figures showing the evolution of the index during the past twelve months are also included. The methodology used for compiling the index is given in Annex. Figures have been rounded to one or two decimal places although they have been calculated to many decimal places.

The methodology used for compiling the index and the changes in the weight structure are given in the annexed  technical notes. Figures have been rounded to one or two decimal places although they have been calculated to many decimal places.

- Evolution of the Construction Price Index, July 2009 to  June 2010

Chart 1 shows the movement of the Construction Price Index from July 2009 to June  2010, with the second quarter of 2009 as base. As from July 2009, the index had a stable trend up to February 2010. A drop in March 2010 occurred due to fall in the prices of cement and steel bars. However, a rising trend is noticed in the index as from April 2010 to June 2010 mainly due to increases in prices of steel bars, block, sand and aggregate.

- Changes in the Construction Price Index  (April to June 2010)

The index remain unchanged in April 2010 when compared to March 2010. But in May, it registered an increase of  1.4% mainly as a result of higher prices of hardcore, sand, block, steel bars and electrical installation.

In June, the index increased by 0.2% mainly  due to a 5.0% increase  in the prices of steel bars  partly  offset by a decrease of 6.0% in the prices of electrical installation.

4.  Changes by Input Categories

Changes by input categories are shown in Tables 1.2 to 1.4.

During the first quarter of 2010, no change was  registered in the  “Labour”, “Hire of plant” and “Transport” sub indices.

The “Materials” sub-index which remained unchanged during the month of April, increased by 2.2%  from 97.5 in April 2010 to 99.7  in May 2010 due to higher prices of hardcore  (1.3%), sand (1.0%), block  (1.0%), steel bars (10.2%), and electrical installation (6.2%).

In June, the sub-index increased by 0.3% as a result of a 5.0% increase in the prices of steel bars, partly offset by a decrease of 6.0% in  the prices of single core cable.

The net monthly contributions of the input categories to the index during the period July 2009 to June 2010 are shown in Table 1.3.

Quarterly averages of the monthly indices by input category and the percentage change from quarter to quarter are shown in Table 1.4.

5.   Changes by Work Category

Changes by work category are shown in Tables 2.2 to 2.4.

The index for all work categories remained unchanged during the month of April 2010.

In May, the increase in the price of hardcore, sand, block, steel bars and electrical installation resulted in increases in the following work categories  “Setting up” (0.1%), “Earthworks” (0.7%), “Concrete” (0.1%), “Reinforcement” (7.2%), “Blockwork” (0.7%), “Rendering to wall/ceiling” (0.1%), “Bed & screed to floor/roof”  (0.1%) and “Electrical installation” (4.9%) .

In June, the 5.0% increase in the price of steel bars resulted in an increase of 3.6% in the “Reinforcement” work category, while the 6.0% decrease in electrical installation resulted in a drop of 4.7% in the “Electrical installation”  work category.

Table 2.3 shows the net monthly contributions of the work categories to the index since July 2009.

Quarterly averages of the monthly indices by work category and the percentage change from quarter to quarter are shown in Table 2.4.

6.   Past Trends

Table 3.1 gives a summary of  the monthly indices, the quarterly and yearly averages as well as the percentage changes in the yearly average since 1999. Indices for the years 1999 to 2001 have been worked out using as base the fourth quarter of 1993, while the base period for the calculation of the index from 2002 up to first quarter 2009 is the fourth quarter of 2001. As from April 2009 the base period used is the second quarter of 2009.

The series are not strictly comparable because of different base periods. However, for some particular purposes, comparison between the series may be necessary. A chain linked series with base period second  quarter 2009 has been worked out and is given in table 3.2.

Central Statistics Office

Ministry of Finance and Economic Development

## Port Louis

August 2010

Technical Note

Methodology for the compilation of the Construction Price Index

- Introduction

A Construction Price Index measures the change in the level of construction prices. The construction industry is very broad and highly diversified with considerable variations from one type of construction to another. This makes it difficult to derive generalized indices that would be applicable to the industry as a whole. Hence, separate indices for the different types of construction need to be compiled. At present, the Central Statistics Office publishes an index that  covers  residential buildings only.

- Types of Construction Price Indices

Different approaches to index number compilation are used depending on the purpose for which the index is required. There are two main types of construction price indices:

# The Output Price Index

In this approach, specific projects representative of the various categories of construction works are selected as models and construction firms are surveyed and asked to provide estimates of the prevailing market prices for each of the projects. As such, the output price indices respond to the changes in prices of materials used and cost of labour, as well as changes in overhead costs and profits.

# The Input Price Index

The index is based on prices of a representative selection of basic inputs (labour, plant, materials and transport) that go into the construction work. Hence, the input price index measures the change in the cost of resources to the contractor, and not the change in the price that the client pays.

The office opted for the input price index  which, though more limiting than the output price index,  is simpler and less expensive to construct and maintain.

- Selection of representative dwelling

Since it would have been too time-consuming and costly to include all major types of residential dwellings, it was decided to restrict the index to a model dwelling, representing the most common type of dwelling in 2007. This model dwelling was determined on the basis of the 2000 Housing Census data and developments assumed to have taken place during the period 2000 to 2007.  The drawings of the prototype model dwelling were provided by the Mauritius Housing Company Ltd. A description of the model is given at paragraph (viii) below.

- Weighting scheme

The quantity survey work to determine the weighting pattern for the index was entrusted to a private Quantity Surveyor following established procedures.

Any given construction consists of an assembly of a certain number of stages or work categories. Sixteen stages or broad work categories were identified and detailed costs of inputs in terms of labour, plant, materials and transport that go into the construction of the selected model were calculated under each of the 16 work categories. The weights have been worked out in such a way that they can be presented in terms of inputs as well as work categories. For publication purposes, weights and sub-indices are shown not only for the 16 work categories, but also for the 4 broad input categories of labour, plant, materials and transport, the “materials” category being further sub-divided into 17 sub-categories.

Changes in the weight structure from 2001 to 2009 are given at the end of this technical note. It is noted that there has been some reclassification within work categories while new ones have been identified. Also within work categories  there has been some changes in the product mix as well as the introduction of some new products.

- Data collection

The data needed for the computation of the index are collected every month from a sample of 50 outlets in 8 regions of the island. Prices are collected in respect of some 109 items, representative of all items that go into the computation of the index.

- Calculation of the Construction Price Index

The Construction Price Index is a weighted average of price relatives of individual items, based on the modified Laspeyres formula:

( Wi (Pit / Pio)    x   100

It     =

( Wi

where	It = index for current period t

Pio  = price of item i at base period 0

Pit  = price of item i at current period t

Wi  = weight of item i

The base period is the 2nd quarter of 2009.

- Uses

- Construction price indices give an indication of the change in the level of prices of construction works. As such, they are used as deflators for the measurement of real growth in the construction sector.

- They are also useful for evaluating cost fluctuations in contracts regarding construction works and for renegotiating owner-tenant agreements.

- Description of model dwelling

The model used is a single storey (ground floor) detached house of 138 square metres (1,485 square feet) in floor area measured at plinth level to the external face of the external walls. The overall area is inclusive of 18.55 square metres (200 square feet) in respect of a garage.

It comprises three bedrooms, a living-dining room, a kitchen, two toilets, a utility room, a bathroom, a verandah and an attached garage. The building has concrete block walls, reinforced concrete flat roof, internal flush plywood doors, aluminium openings for windows and entrance door, screeded floor and roof, tiling to floor and walls of w.c. and bathroom and kitchen worktop; the ceilings and walls are rendered and painted both internally and externally. Plumbing, sanitary installation and electrical installation are included as well as drainage which is to be connected to the sewerage system.

Provision has been made, in the form of more substantial foundations and of stub columns on the roof, for converting the single into a two-storey house eventually. Site works are restricted to spreading and leveling surplus excavated material around the site.

The index excludes the cost of the building permit and the draughtman’s fee.

It is assumed that although the house is not constructed by a contractor, the client has recourse to the services of a foreman.

# Text boxes

Contact person: 	Ms. F.Victor

Senior  statistical officer

Central Statistics Office

LIC Centre

Port-Louis

Tel: 212 2316/17

Fax: 211 4150

Email: cso_construction@mail.gov.mu