# CONSTRUCTION PRICE INDEX

(Input Cost Index for the construction of a single storey house)

3rd Quarter 2013

1.  Introduction

This issue of the Economic and Social Indicators presents the monthly Construction Price Index (residential) for the third quarter of 2013 with second quarter 2009 as base period. Figures showing the evolution of the index during the past twelve months are also included.

The methodology used for compiling the index is given in the annexed technical notes. Figures have been rounded to one or two decimal places although they have been calculated to many decimal places.

2.  Evolution of the Construction Price Index

(October 2012 to September 2013)

Chart 1 shows the movement of the Construction Price Index from October 2012 to September 2013 with the second quarter of 2009 as base. The index which stood at 108.8 in October 2012 remained unchanged in November 2012 and increased to 108.9 in December 2012 due to increases in the prices of ceramic tiles. In January 2013, the index increased to 109.8 mainly as a result of higher wages and in February 2013 to 110.5 mostly due to increases in the prices of cement. The index registered a slight decrease to 110.4 in March 2013. In April 2013, the index rose to 110.9, remained at the same level in May 2013. It increased to 111.0 in June 2013 and remained unchanged in July 2013. In August 2013, it went up to 111.1 and remained at the same level in September 2013.

3.  Changes in the Construction Price Index

(July to September 2013)

The Construction Price Index, which stood at 111.0 at the end of June 2013, remained at the same level in July 2013 following an increase of 0.1% in the prices of steel bars offset by a decrease of 0.6% in the prices of plumbing.

In August 2013, the index registered an increase of 0.1% to reach 111.1 mainly as a result of increases of 1.6% in the rate for hire of plants coupled with increases of 0.4% in the prices of both block and timber carpentry partly offset by a drop of 0.1% in the prices of steel bars.

In September 2013, the index remained at 111.1 although an increase of 1.1% was observed in the price of sanitary installation.

Compared to the corresponding months of the previous year, the index shows overall increases of 2.1% for July 2013, 2.2% for August 2013 and 2.1% for September 2013 (Table 1.3).

4.  Changes by Input Categories

Changes by input categories are shown in Tables 1.1 to 1.5.

During the third quarter of 2013, no change was registered in the “Labour” and “Transport” sub-indices.

The ‘Hire of plant” sub-index which stood at 105.8 in June 2013 remained unchanged in July, increased by 1.6%  to reach 107.5 in August 2013 due to higher rates for hire of formwork for decorative column. It remained unchanged in September 2013.

The “Materials” sub-index which stood at 111.7 in June 2013 remained at the same level up to September 2013. However, on a monthly basis, an increase of 0.1% was registered in the prices of steel bars offset by a decrease of 0.6% in the prices of plumbing in July 2013. In August 2013, the prices of both block and timber carpentry increased by 0.4% whilst the prices of steel bars decreased by 0.1%. In September 2013, the prices of sanitary installation increased by 1.1%.

The net monthly contributions of the input categories to the index during the period October 2012 to September 2013 are shown in Table 1.4.

Quarterly averages of the monthly indices by input category and the percentage change from quarter to quarter are shown in Table 1.5.

5.  Changes by Work Category

Changes by work category are shown in Tables 2.1 to 2.5.

During the month of July 2013, the 0.1% increase in the prices of steel bars resulted in an increase of 0.1% in the “Reinforcement” work category whilst the 0.6% drop in the prices of plumbing resulted in a decrease of 0.2% in the “Plumbing & Drainage” work category.

In August 2012, the “Formwork” work category registered an increase of 0.8% following increases of 1.6% in the rates for the hire of formwork for decorative columns and 0.4% in the prices of timber carpentry. The “Blockwork” work categories increased by 0.2% as a result an increase of 0.4% in the prices of block. The “Reinforcement” work category decreased by 0.1% due to a decrease of 0.1% in the prices of steel bars.

In September 2012, the “Plumbing & Drainage” work category increased by 0.5% due to higher prices of sanitary installation (1.1%).

Table 2.4 shows the net monthly contributions of the work categories to the index since October 2012.

Quarterly averages of the monthly indices by work category and the percentage changes from quarter to quarter are shown in Table 2.5.

6.  Past Trends

Table 3.1 summarises the monthly indices, the quarterly and yearly averages as well as the percentage changes in the yearly average since 2002. The base period for the calculation of the index as from 2002 up to the first quarter of 2009 is the fourth quarter of 2001. As from April 2009 the base period used is the second quarter of 2009.

The series are not strictly comparable because of different base periods. However, for some particular purposes, comparison between the series may be necessary. A chain linked series with base period second quarter 2009 has been worked out and is given in Table 3.2.

Statistics Mauritius

Ministry of Finance and Economic Development

Port Louis

October 2013

Technical Note

Methodology for the compilation of the Construction Price Index

- Introduction

A Construction Price Index measures the change in the level of construction prices. The construction industry is very broad and highly diversified with considerable variations from one type of construction to another. This makes it difficult to derive generalized indices that would be applicable to the industry as a whole. Hence, separate indices for the different types of construction need to be compiled. At present, Statistics Mauritius publishes an index that covers  residential buildings only.

- Types of Construction Price Indices

Different approaches to index number compilation are used depending on the purpose for which the index is required. There are two main types of construction price indices:

# The Output Price Index

In this approach, specific projects representative of the various categories of construction works are selected as models and construction firms are surveyed and asked to provide estimates of the prevailing market prices for each of the projects. As such, the output price indices respond to the changes in prices of materials used and cost of labour, as well as changes in overhead costs and profits.

# The Input Price Index

The index is based on prices of a representative selection of basic inputs (labour, plant, materials and transport) that go into the construction work. Hence, the input price index measures the change in the cost of resources to the contractor, and not the change in the price that the client pays.

The office opted for the input price index  which, though more limiting than the output price index,  is simpler and less expensive to construct and maintain.

- Selection of representative dwelling

Since it would have been too time-consuming and costly to include all major types of residential dwellings, it was decided to restrict the index to a model dwelling, representing the most common type of dwelling in 2007. This model dwelling was determined on the basis of the 2000 Housing Census data and developments assumed to have taken place during the period 2000 to 2007.  The drawings of the prototype model dwelling were provided by the Mauritius Housing Company Ltd. A description of the model is given at paragraph (viii) below.

- Weighting scheme

The quantity survey work to determine the weighting pattern for the index was entrusted to a private Quantity Surveyor following established procedures.

Any given construction consists of an assembly of a certain number of stages or work categories. Sixteen stages or broad work categories were identified and detailed costs of inputs in terms of labour, plant, materials and transport that go into the construction of the selected model were calculated under each of the 16 work categories. The weights have been worked out in such a way that they can be presented in terms of inputs as well as work categories. For publication purposes, weights and sub-indices are shown not only for the 16 work categories, but also for the 4 broad input categories of labour, plant, materials and transport, the “materials” category being further sub-divided into 17 sub-categories.

Changes in the weight structure from 2001 to 2009 are given at the end of this technical note. It is noted that there has been some reclassification within work categories while new ones have been identified. Also within work categories there has been some changes in the product mix as well as the introduction of some new products.

- Data collection

The data needed for the computation of the index are collected every month from a sample of 50 outlets in 8 regions of the island. Prices are collected in respect of some 109 items, representative of all items that go into the computation of the index.

- Calculation of the Construction Price Index

The Construction Price Index is a weighted average of price relatives of individual items, based on the modified Laspeyres formula:

( Wi (Pit / Pio)    x   100

It     =

( Wi

where	It = index for current period t

Pio  = price of item i at base period 0

Pit  = price of item i at current period t

Wi  = weight of item i

The base period is the 2nd quarter of 2009.

- Uses

- Construction price indices give an indication of the change in the level of prices of construction works. As such, they are used as deflators for the measurement of real growth in the construction sector.

- They are also useful for evaluating cost fluctuations in contracts regarding construction works and for renegotiating owner-tenant agreements.

- Description of model dwelling

The model used is a single storey (ground floor) detached house of 138 square metres (1,485 square feet) in floor area measured at plinth level to the external face of the external walls. The overall area is inclusive of 18.55 square metres (200 square feet) in respect of a garage.

It comprises three bedrooms, a living-dining room, a kitchen, two toilets, a utility room, a bathroom, a verandah and an attached garage. The building has concrete block walls, reinforced concrete flat roof, internal flush plywood doors, aluminium openings for windows and entrance door, screeded floor and roof, tiling to floor and walls of w.c. and bathroom and kitchen worktop; the ceilings and walls are rendered and painted both internally and externally. Plumbing, sanitary installation and electrical installation are included as well as drainage which is to be connected to the sewerage system.

Provision has been made, in the form of more substantial foundations and of stub columns on the roof, for converting the single into a two-storey house eventually. Site works are restricted to spreading and leveling surplus excavated material around the site.

The index excludes the cost of the building permit and the draughtman’s fee.

It is assumed that although the house is not constructed by a contractor, the client has recourse to the services of a foreman.

# Text boxes

Contact persons: 	Mr. L. Persand (Statistician)

Ms. F. Victor (Senior Statistical Officer)

Statistics Mauritius

LIC Centre

Port-Louis

Tel: 212 2316/17

Fax: 213 0234

Email: cso_construction@mail.gov.mu