# CONSTRUCTION PRICE INDEX

(Input Cost Index for the construction of a single storey house)

4th Quarter 2015

1.  Introduction

This issue of the Economic and Social Indicators presents the monthly Construction Price Index (residential) for the fourth quarter of 2015 with second quarter 2009 as base period. Figures showing the evolution of the index during the past twelve months are also included.

The methodology used for compiling the index is given in the annexed technical notes. Figures have been rounded to one or two decimal places although they have been calculated to many decimal places.

2.  Evolution of the Construction Price Index

(January to December 2015)

Chart 1 shows the movement of the Construction Price Index from January to December 2015 with the second quarter of 2009 as base. The index which stood at 113.8 in January decreased slightly to 113.7 in February 2015 and then increased to 113.9 in March 2015. In April 2015, the index increased to 114.0 and remained unchanged in May 2015. It then increased to 114.1 in June 2015 but remained at the same level in July 2015. In August 2015 the index increased to 114.2 and remained at the same level up to October 2015. In November 2015 the index dropped to 114.0, followed by another drop to reach 113.8 in December 2015.

3.  Changes in the Construction Price Index

(October to December 2015)

The Construction Price Index, which stood at 114.2 at the end of September 2015 remained at the same level in October 2015. Decreases were noted in the prices of steel bars (-1.2%) and sanitary installation (-0.4%); while increases were noted in the prices of ceramic tiles (+2.5%), timber carpentry (+0.2%) and metal openings (+0.2%).

In November 2015, the index dropped to 114.0 as a result of decreases in the prices of steel bars (-1.2%) and timber carpentry (-0.3%), partly offset by an increase in the prices of sanitary installation (+0.2%).

The overall index registered another drop to reach 113.8 in December 2015 following decreases of 1.7% in the prices of steel bars and 0.2% in the prices of metal openings.

Compared to the corresponding months of the previous year, the index shows overall increases of 1.6% for October 2015, 1.5% for November 2015 and 1.4% for December 2015 (Table1.3).

4.  Changes by Input Categories

Changes by input categories are shown in Tables 1.1 to 1.5.

During the fourth quarter of 2015, no change was registered in the “Labour”, “Hire of plant” and “Transport” sub-indices.

The “Materials” sub-index which stood at 112.6 in September 2015 registered a slight drop of 0.1% to reach 112.5 in October 2015. This drop is mainly due to decreases of 1.2% in the prices of steel bars and 0.4 % in the prices of sanitary installation, partly offset by increases of 2.5% in the prices of ceramic tiles, 0.2% in the prices of timber carpentry and 0.2% in the prices of metal openings.

In November 2015, the sub-index registered a drop of 0.2% to reach 112.3 as a result of a decrease in the prices of steel bars (-1.2%) and timber carpentry
(-0.3%), partly offset by an increase of 0.2% in the prices of sanitary installation.

The sub-index registered another drop of 0.2% to reach 112.0 in December 2015 following decreases of 1.7% in the prices of steel bars and 0.2% in the prices of metal openings.

The net monthly contributions of the input categories to the index during the period January to December 2015 are shown in Table 1.4.

Quarterly averages of the monthly indices by input category and the percentage change from quarter to quarter are shown in Table 1.5.

5.  Changes by Work Category

Changes by work category are shown in Tables 2.1 to 2.5.

During the month of October 2015, the “Reinforcement” work category registered a drop of 0.8% following a decrease of 1.2% in the prices of steel bars. The “Plumbing and Drainage” work category decreased by 0.2% as a result of a decrease in the prices of sanitary installation (-0.4 %). The increase of 2.5% in the prices of ceramic tiles resulted in an increase of 1.2% in the “Tiling” work category. Higher prices of metal openings (0.2%) and timber carpentry (0.2%) affected the “Metal openings” (0.1%) and “Formwork” (0.1%) work categories.

In November 2015, the “Reinforcement” work category dropped by 0.9% due to a decrease in the price of steel bars (-1.2%). The “Formwork” work category registered a drop of 0.1% following a decrease of 0.3% in the prices of timber carpentry. The “Plumbing and 

Drainage” work category increased by 0.1% as a result an increase in the prices of sanitary installation (0.2%).

In December 2015, the “Reinforcement” work category registered another drop of 1.2% due to a further decrease of 1.7% in the prices of steel bars. The 0.2% drop in the prices of metal openings resulted in a decrease of 0.1% in the “Metal Openings” work category.

Table 2.4 shows the net monthly contributions of the work categories to the index since January 2015.

Quarterly averages of the monthly indices by work category and the percentage changes from quarter to quarter are shown in Table 2.5.

6.  Past Trends

Table 3.1 summarises the monthly indices, the quarterly and yearly averages as well as the percentage changes in the yearly average since 2003. The base period for the calculation of the index as from 2002 up to the first quarter of 2009 is the fourth quarter of 2001. As from April 2009 the base period used is the second quarter of 2009.

The series are not strictly comparable because of different base periods. However, for some particular purposes, comparison between the series may be necessary. A chain linked series with base period second quarter 2009 has been worked out and is given in Table 3.2.

Statistics Mauritius

Ministry of Finance and Economic Development

Port Louis

January 2016

# Text boxes

Contact persons: 	Mr. L. Persand (Statistician)

Ms. F. Victor (Senior Statistical Officer)

Statistics Mauritius

LIC Centre

Port-Louis

Tel: 208 1800

Fax: 213 0234

Email: cso_construction@ govmu.org